## Slide 1: Temperature controlled Fan speed with Fire alarm system

## Slide 2
Farhan Shahriar
Department of Computer Science & Engineering
Brac University
ID-14201016
Mahmudul Hasan Shakil
Department of Computer Science & Engineering
Brac University
ID-16301026
Sayed Mahmud Khan
Department of Computer Science & Engineering
Brac University
ID-16301023
Farhan Anjum
Department of Computer Science & Engineering
Brac University
ID-17301184

## Slide 3: Introduction
Arduino based fan
Built in alarm system
Cheap

## Slide 4: Equipments
● 12-volt table fan
● LM35 temperature sensor
● Arduino microcontroller
● A led
● A buzzer
● An IRF 540n n-channel mosfet
● 12-volt dc battery
● A switch
A lighter

## Slide 5: procedure
● The LM35 sensor continuously senses the room temperature and keeps on giving an analog voltage between 0 volt and 5 volts.
● This output voltage is connected with a general-purpose microcontroller Arduino Uno’s A0 analog pin. This pin of Arduino is used to read analog signals.
● A led and a buzzer is connected respectfully with Arduino’s 8 and 7 pin which will indicate any alarming temperature reading of lm35 sensor. They are always connected and automatically switch on/off depending on the readings.
● Any temperature reading less than the cutoff temperature is used to control the speed of the fan using a PWM pin, pin no 6 of the Arduino. PWM stands for pulse width modulator. It sends pulses of varying duty cycles to produce an analog signal.
● The analog signal is also a signal between 0 volt and 5 volts.
● This signal is sent to the gate of a mosfet.
● Mosfets can control the flow of current. They work as voltage divider and can create variable resistance to reduce the voltage drop across the fan and thus can control its motor.
● The fan is connected a dc voltage source to give it the power to conduct.

## Slide 6: procedure
The fan is also connected to a switch to switch on and off the fan’s connection manually.
● If the switch is off only the functions of the fan will not work. The alarm system would still be conducting.
● A 20x4 LCD monitor is connected with the Arduino.
● It shows the room temperature along with the fan speed and other necessary info.

## Slide 7: Calculation
Arduino gives value of 1024 when 5000 millivolts is received
Arduino gives value of 1 when (5000/1024) millivolt is received
So, Arduino gives value of x when ((5000/1024) *x) millivolts is received.
Now, as 10 millivolts is given per degree centigrade,
Temperature = ((5000/1024) *x)/10.
If Arduino receive 5 volts at PWM it sends 255 from the pin
So ” “ 1 “ “ “ “ 255/5=51

## Slide 8: Any question